## Slide 1
A S R Pavan
Scientist ‘B’
NIELIT Calicut
Internship on DSP & its Application
NIELIT Calicut M01_MATLAB & Digital Signal Processing STED

## Slide 2
Lecture Structure
NIELIT Calicut M01_MATLAB & Digital Signal Processing STED
Video Lecture
PPT Slide

## Slide 3
Day 1: 3hrs
Day 2: 3hrs
Day 3: 3hrs
Day 4: 3hrs
Day 5: 3hrs
01
Basics
02
Data Operations
03
Plotting data
04
Signal Processing
05
File Handling
Module_01: Time Line
NIELIT Calicut M01_MATLAB & Digital Signal Processing STED

## Slide 4
MATLAB Installation
Link: provided in urls.txt file
30 days free trail period is provided by MATLAB
MATLAB Online: can be accessed through any standard web browser.
  No need for downloads or installations
  Access to MATLAB and Simulink
  https://in.mathworks.com/products/matlab-online.html
Detailed installation of matlab installation pdf is attached.
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day01 STED

## Slide 5
About MATLAB
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day01 STED
MATLAB is a high-performance language for technical computing.
It integrates computation, visualization, and programming in an
easy-to-use environment
Some MATLAB use cases include:
  Math and computation
  Algorithm development
  Data analysis, exploration, and visualization
  Scientific and engineering graphics
  Modelling, simulation, and prototyping
  Application development, including Graphical User Interface building
Notes: MATLAB is an interactive, matrix-based system for scientific and engineering numeric computation and visualization. Its strength lies in the fact that complex numerical problems can be solved easily and in a fraction of the time required by a programming language such as Fortran or C. It is also powerful in the sense that, with its relatively simple programming capability, MATLAB can be easily extended to create new commands
and functions.
The basic MATLAB program is further enhanced by the availability of numerous toolboxes (collections of specialized functions in specific topics) over the years.

## Slide 6
MATLAB Basics
MATrix LABoratory
  The basic variable is a matrix or an array.
MATLAB Window
Built-in functions
Variable creation
Hiding Output
Clearing commands
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day01 STED
Notes: Scripts block mode of operation. In MATLAB, this mode is implemented using a script file called an m-file (extension .m), which is only a text file that contains each line of the file as though
you typed them at the command prompt. The script file must be in the current directory or in the directory of the path environment.
Functions The second construct of creating a block of code is through subroutines. These are called functions, which also allow us to extend the capabilities of MATLAB. In fact, a major portion
of MATLAB is assembled using function files in several categories and using special collections called toolboxes. Functions are also m-files (with extension .m). A major difference between script
and function files is that the first executable line in a function file begins with the keyword function followed by an output-input variable declaration.

## Slide 7
MATLAB Basics
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day01 STED

## Slide 8
MATLAB Basics
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day01 STED
Display Windows: MATLAB has three display windows. They are 1. A Command Window which is used to enter commands 2. A Graphics Window which is used to display plots and graphs. 3. An Editor Window which is used to create and modify m-files. m-files are files that contain a program or script of MATLAB commands.

## Slide 9
Inputs and Outputs
Matrix Operations
Creating a matrix
Scalar functions
Vector functions
Matrix functions
Colon operator
Linspace
... or ellipsis
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day02 STED

## Slide 10
Inputs and Outputs
Built-in array functions
Matrix operators vs Array operators
Round-off functions
Predefined variables
Help & Documentation usage
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day02 STED

## Slide 11
Scripts vs functions
Scripts vs functions
  Ignoring function outputs
Live scripts
Input from Command Window
Displaying on Command Window
Conditional Statements: if, if-else, for, …
Conditional equality(==)
Logical Operators & Relational Operators
Break Points
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day02 STED

## Slide 12
Structures and cell arrays
Structures: Array that groups related data using fields.
  Fields can be accessed using dot operator.
  Fields can be of different type and size
Cell Arrays: similar to structures that can contain data of varying types and sizes.
  use class function to see what it returns to.
  Accessing cell data using {}
Conversion from cell array to structure array and vice-versa.
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day02 STED

## Slide 13
Saving workspace data
Saving Workspace
Loading Workspace
Saving Command window
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day02 STED

## Slide 14
Plotting data
Plot Command
Grid
Axis
Labeling
Title
Hold
Subplots
Color, line-style & Marker style
Legend
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day03 STED
Notes: For plotting a set of discrete numbers (or discrete-time signals), we will use the stem command, which displays data values as a stem, that is, a small circle at the end of a line connecting it to the horizontal axis. The circle can be open (default) or filled (using the option ’filled’).

## Slide 15
Generation of signals
Sinusoidal signal
Random signal
Basic signal operations
AM-DSBFC
  Under-modulated
  Over-modulated
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day03 STED
Notes: The rand(1,N) generates a length N random sequence whose elements are uniformly distributed between [0, 1].
The randn(1,N) generates a length N Gaussian random sequence with mean 0 and variance 1.
fliplr command

## Slide 16
Polynomials
How to write Polynomial as a vector
Finding the Value of a polynomial at a specified Point : polyval
Finding the roots of Polynomial : roots
Generate Polynomial for the given roots : poly
Polynomial: ax^n + bx^(n-1) + cx^(n-2)+ ……+px + q
If order of polynomial is ‘n’ the no. of terms in equation is ‘n+1’
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day03 STED

## Slide 17
Basic DSP functions
Interpolation
Decimation
Generating Analytic signal
Magnitude of complex signal
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day03 STED

## Slide 18
Transforms
DFT algorithms
DFT using FFT algorithm
  Single sided spectrum
  Double sided spectrum
  Removing mirror-image from spectrum
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day03 STED
Notes: Chapter 8 : Efficient Computation of the DFT: Fast Fourier Transform Algorithms
(Digital Signal Processing Principles, Algorithms and applications 4th edition by John G Proakis, Dimitris G Manolakis )
to compute all N values of the DFT requires complex multiplications (1 complex multiplication = 4 real multiplications) and complex additions(4*() real additions).
by taking advantage of the symmetry and periodicity properties of the exponential factors of twiddle factor,we can reduce the number of complex multiplications needed to compute the DFT
For radix-2 N-pt FFT For N = 2" , there are N /2 butterflies per stage of the computation process and log2 N stages. Therefore, as previously indicated, the total number of complex multiplications is (N/2) log2 N and complex additions is N log2 N.
An important application of the FFT algorithm is in FIR linear filtering of long data sequences. we described two methods, the overlap-add and the overlapsave methods for filtering
a long data sequence with an FIR filter, based on the use of the DFT.
A Linear Filtering Approach to Computation of the DFT : The Goertzel Algorithm, chirp-z transform algorithm
There are some applications where only a selected number of values of the DFT are desired, but the entire DFT is not required. In such a case, the FFT algorithm may no longer be
more efficient than a direct computation of the desired values of the DFT. In fact, when the desired number of values of the DFT is less than log2 N,a direct computation of the
desired values is more efficient.
The recognition that the DFT can be arranged and computed as a linear convolution is also highly significant. Goertzel (1968) indicated that the DFT can be computed via linear filtering,
although the computational savings of this approach is rather modest
Goertzel Algorithm:
chirp-z: chirp-z transform algorithm, which is suitable for evaluating the z-transform of a set of data on a variety of contours in the z-plane.
Chapter 8 : Efficient Computation of the DFT: Fast Fourier Transform Algorithms
(Digital Signal Processing Principles, Algorithms and applications 4th edition by John G Proakis, Dimitris G Manolakis )
to compute all N values of the DFT requires 𝑁^2 complex multiplications (1 complex multiplication = 4 real multiplications) and 𝑁^2 −𝑁 complex additions(4*(𝑁^2 −𝑁 ) real additions).
by taking advantage of the symmetry and periodicity properties of the exponential factors of twiddle factor,we can reduce the number of complex multiplications needed to compute the DFT
For radix-2 N-pt FFT For N = 2" , there are N /2 butterflies per stage of the computation process and log2 N stages. Therefore, as previously indicated, the total number of complex multiplications is (N/2) log2 N and complex additions is N log2 N.
An important application of the FFT algorithm is in FIR linear filtering of long data sequences. we described two methods, the overlap-add and the overlapsave methods for filtering
a long data sequence with an FIR filter, based on the use of the DFT.
A Linear Filtering Approach to Computation of the DFT : The Goertzel Algorithm, chirp-z transform algorithm
There are some applications where only a selected number of values of the DFT are desired, but the entire DFT is not required. In such a case, the FFT algorithm may no longer be
more efficient than a direct computation of the desired values of the DFT. In fact, when the desired number of values of the DFT is less than log2 N,a direct computation of the
desired values is more efficient.
The recognition that the DFT can be arranged and computed as a linear convolution is also highly significant. Goertzel (1968) indicated that the DFT can be computed via linear filtering,
although the computational savings of this approach is rather modest
Goertzel Algorithm:
chirp-z: chirp-z transform algorithm, which is suitable for evaluating the z-transform of a set of data on a variety of contours in the z-plane.

## Slide 19
DSP
DSP hardware allows programmable operations
  Through software we can easily modify the processing functions.
  It offers greater degree of flexibility in system design.
  Higher order of precision can be achievable compared to other processing systems.
  Digital signals are easy to store and reproduce.
DSP is not proper solution for all signal processing problems
  For extremely wide band-width signals real-time processing is a requirement.
  For these signals, analog or optical signal processing is the only possible solution.
  If the Digital circuits have sufficient speed to perform the DSP is preferred.
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day03 STED
Notes: Digital Signal Processing Principles, Algorithms and applications 4th edition by John G Proakis, Dimitris G Manolakis Page no. 1(20/1103)

## Slide 20
Filters & Windowing Techniques
Writing filters using own scripts
Using Filter design tools
Using one filter coefficients for realization of other filter
Windowing techniques
Generating using own scripts
Using designer tools
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day04 STED
Notes: DSP 4th ed. by prokias
the term filter to describe a linear time-invariant system used to perform spectral shaping or frequency-selective filtering.
Filtering is used in digital signal processing in a variety of ways, such as removal of undesirable noise from desired signals, spectral shaping such as equalization of communication channels, signal
detection in radar, sonar, and communications, and for performing spectral analysis of signals, and so on.
Filters are usually classified according to their frequency-domain characteristics as lowpass, highpass, bandpass, and bandstop or band-elimination filters.
Ideal filters have a constant magnitude characteristic and a linear phase characteristic within their passband. In all cases, such filters are not physically realizable but serve as a mathematical idealization of practical filters.
*2:{ 48: If the unit impulse response of an LTI system is of finite duration, then the system is called a finite-duration impulse response (or FIR) filter.
Filter: keyword: A function called filter is available to solve difference equations numerically, given the input and the difference equation coefficients.
y = filter(b,a,x) where b = [b0, b1, ..., bM]; a = [a0, a1, ..., aN]; are the coefficient arrays of x and y respectivelyand
x is the input sequence array. The output y has the same length as input x. One must ensure that the coefficient a0 not be zero.
Impz: keyword for impulse response }
Pg 334: Suppose that we have designed a prototype lowpass filter with impulse response hlp(n). By using the frequency translation property of the Fourier transform,
it is possible to convert the prototye filter to either a bandpass or a highpass filter. Frequency transformations for con verting a prototype lowpass filter into a
filter of another type are described in detail in Section 10.3.
we present a simple frequency transformation for converting a lowpass filter into a highpass filter
If hlp(n) denotes the impulse response of a lowpass filter with frequency response Hlp(W), a highpass filter can be obtained by translating Hlp(W) by pi radians
i.e., replacing W by W – pi eg: pg 335
which type of filter to design, FIR or IIR, depends on nature of the problem and on the specifications of the desired frequency response.
In practice, FIR filters are employed in filtering problems where there is a requirement for a linear-phase characteristic within the passband of the filter. If there is no requirementfor a Hnear-phase characteristic, either an IIR or an FIR filter may be employed.
an IIR filter has lower sidelobes in the stopband than an FIR filter having the same number of parameters. For this reason,if some phase distortion is either tolerable or unimportant,
an IIR filter is preferable, primarily because its implementation involves fewer parameters, requires less memory and has lower computational complexity. any ideal filter is noncausal but we can design only causal filters.
ideal filters are noncausal and hence physically unrealizable for real-time signal processing applications.
Causality implies that the frequency response characteristic H (w) of the filter cannot be zero, except at a finite set of points in the frequency range.
The width of the passband is usually called the bandwidth of the filter.
Diff. Between filters and windows:
A filter would be a convolution of a signal with another. In a technical sense, a window has a fixed (supposedly short) size and is seen as "cutting out" a short part of the signal.
Often, a DFT would follow.
A filter scales the spectrum with a known frequency response. A window will filter the spectrum instead.
Filters and window functions often (but not always) have different design goals. For example, in a filter you would have rather large bandwidths.
Windows percieved as useful have a small bandwidth (often, just a few samples).
a filter is seen by time domain convolution (for a linear system) while windowing is time domain multiplication.
window an incoming signal (i know earlier i said in time domain only but this is also applicable to frequency domain), that becomes a filter which windows the signal

## Slide 21
Basic statastical data operations
Mean
Standard deviation
Supression of side lobes using windowing techniques
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day04 STED
Notes: https://in.mathworks.com/help/matlab/creating_guis/choose-components-for-your-app-designer-app.html

## Slide 22
File handling in MATLAB
Exporting data in to excel file or text file
Importing data from excel file or text file
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day05 STED

## Slide 23
GUI
GUI design
  Creating basic user dialog box
  Creating dailog box for selection of file
  switch-case user dialog box
Creating Stand-alone application
Creating MATLAB APP
Convertion of MATLAB function in to c-code
Using MATLAB Convert C-code in other IDE
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day05 STED

## Slide 24
References
Digital Signal Processing John G. Proakis, Dimitris K Manolakis - (2007, Pearson)
Digital Signal Processing Using Matlab_ A Problem Solving Companion. Vinay K. Ingle, John G. Proakis 4 ed.-Cengage Learning (2016)
https://in.mathworks.com/help/matlab/index.html
NIELIT Calicut M01_MATLAB & Digital Signal Processing_Day05 STED

## Slide 25
Interview Q & A Discussion
Q&A
NIELIT Calicut M01_MATLAB & Digital Signal Processing STED

## Slide 26
Doubts
Q&A
NIELIT Calicut M01_MATLAB & Digital Signal Processing STED

## Slide 27
End of the Module
Thank You
NIELIT Calicut M01_MATLAB & Digital Signal Processing STED